## Slide 1: Multiplexed Illumination for Scene Recovery in the Presence of Global Illumination
Jinwei Gu1, Toshihiro Kobayashi2,
Mohit Gupta3, Shree K. Nayar3
1Rochester Institute of Technology, 2Canon Inc., 3Columbia University
http://www.cis.rit.edu/jwgu/research/demux
Notes: I will present our work on multiplexed illumination for scene recovery in the presence of global illumination.

## Slide 2
source
surface
P
Direct and Global Illumination
camera
Slide courtesy of Nayar, et al. 2006
Notes: Let me first explain what is global illumination.
In this scene, the light from the source to the camera via scene point P, has multiple paths.

## Slide 3
source
surface
P
Direct and Global Illumination
A
A : Direct
camera
Slide courtesy of Nayar, et al. 2006
Notes: First, the light from the source is reflected on P and directly reaches to the camera. This is called direct illumination.

## Slide 4
source
surface
P
Direct and Global Illumination
A
A : Direct
B
B : Interrelection
camera
Slide courtesy of Nayar, et al. 2006
Notes: Second, the light bounces off another scene point and it’s reflected again at P to the camera. This is called inter-reflection.

## Slide 5
source
surface
P
Direct and Global Illumination
A
A : Direct
B
B : Interrelection
C
C : Subsurface
camera
Slide courtesy of Nayar, et al. 2006
Notes: The light can also penetrate the surface and scatter underneath it, come out to the camera. This is called sub-surface scattering.

## Slide 6
source
surface
P
Direct and Global Illumination
A
A : Direct
B
B : Interrelection
C
C : Subsurface
D
participating
medium
D : Volumetric
camera
Slide courtesy of Nayar, et al. 2006
Notes: If there is a participating medium such as haze and fog, this produces volumetric scattering.

## Slide 7
source
surface
P
Direct and Global Illumination
A
A : Direct
B
B : Interrelection
C
C : Subsurface
D
participating
medium
D : Volumetric
camera
Slide courtesy of Nayar, et al. 2006
Notes: All these secondary light matter interactions, they are called global illumination.

## Slide 8: Global Illumination is Everywhere
Notes: Global illumination is everywhere in our real world, as shown in these examples. In fact, it is nearly impossible to find a scene that does not have global illumination.
However, many computer vision algorithm often ignore global illumination and assume there is only direct illumination.

## Slide 9: Global Illumination in Scene Recovery
Bias in shape recovery and material estimation
Structured Light Recovery of
a Bowl (Grey Code)
[Gupta, et al., 2010]
Color Bleeding in
Cornell Box
Error Due to
Inter-reflection
Notes: If we simply ignore global illumination, we will often introduce significant errors in shape recovery and material estimation.
The left image shows an example where the inter-reflection of a bowl causes error in the depth recovery.
The right image shows the color bleeding of the Cornell box scene, yet both boxes have neutral reflectance.

## Slide 10: Related Work
Direct/Global Separation for a Single Source
Illumination Multiplexing
[Nayar, 2006]
[Seitz, 2005]
[Chen, 2008]
[Harwit, 1979] [Schechner, 2003] [Ratner, 2007]
surface
camera
source
[Gupta, 2009] …
Notes: The problem of global illumination has been solved for one light source.
In particular, Nayar et al. proposed a method which uses high-frequency light patterns to separate direct and global illumination for a single light source.
Followed up works extend this method to structured light range scanning, and take into projector defocus.
However, there is no general theory dealing with multiple light sources.
Since we are dealing with multiple light sources, our work is also related to illumination multiplexing, which shows SNR benefits by multiplexing lights and de-multiplexing afterwards. We extend illumination multiplexing in the presence of global illumination.

## Slide 11: Multiple Sources for Scene Recovery
A variety of computer vision applications
Photometric Stereo
Structured Light
Range Scanning
BRDF Estimation
Notes: Before we explain details of our algorithm, we want to emphasize there are many computer vision algorithms which require multiple light sources for scene recovery.
For example, photometric stereo requires at least 3 lights to recover surface normals.
Multiple structured light patterns are used to recover depths.
People uses multiple lights and cameras to estimate BRDFs of materials.
In these applications, how should we deal with the global illumination problem?

## Slide 12: Multiple Sources: Sequential Separation
Require N times images for N light sources
Notes: One straightforward solution is to apply the direct/global separation method for a single source sequentially for N lights.

## Slide 13: Multiple Sources: Sequential Separation
Require N times images for N light sources
L1
L2
L3
Surface: V-groove
Notes: For example, we have a V-groove scene under three lights.

## Slide 14: Multiple Sources: Sequential Separation
Require N times images for N light sources
L1
L2
L3
Surface: V-groove
Notes: Once we apply the separation three times, we get the corresponding direct and global components.

## Slide 15: Multiple Sources: Sequential Separation
Require N times images for N light sources
L1
L2
L3
Surface: V-groove
Notes: And repeat it for each light.

## Slide 16: Multiple Sources: Sequential Separation
Require N times images for N light sources
L1
L2
L3
Surface: V-groove
Notes: This will require N times images.
Can we do better than this sequential method?

## Slide 17: Multiple Sources Separation: Motivation
We should do better than sequential separation, because
Notes: We have two key observations.

## Slide 18: Multiple Sources Separation: Motivation
L1
L2
L3
Surface: V-groove
We should do better than sequential separation, because
  Only the N direct illuminations are needed for scene recovery
Notes: First, for the scene recovery applications, we often only need the N direct illumination components.

## Slide 19: Multiple Sources Separation: Motivation
L1
L2
L3
Surface: V-groove
We should do better than sequential separation, because
  Only the N direct illuminations are needed for scene recovery
+
+
Sum of Global
Illuminations
Notes: We do not care about the global illumination. Thus there are N+1 unknowns in total. We should be able to solve for them with fewer images than sequential method.

## Slide 20: Multiple Sources Separation: Motivation
L1
L2
L3
Surface: V-groove
We should do better than sequential separation, because
  Only the N direct illuminations are needed for scene recovery
  (Potential) Multiplexed advantage in SNR
Sum of Global
Illuminations
Notes: Second, since we have multiple light sources, we can expect there could be multiplexed advantage in terms of SNR if we illuminate them simultaneously.
These two key observations motivate us to look into the problem of direct/global separation for multiple light sources.

## Slide 21: A Theoretical Lower Bound for N Sources
N+1 images are needed to extract the N direct components
Notes: We first found a theoretical lower bound for the number of images we need.
For N light sources, we need at least N+1 images to extract the N direct components. And if light sources can project perfect step edges, N+1 images are sufficient.

## Slide 22: A Theoretical Lower Bound for N Sources
N+1 images are needed to extract the N direct components
L1
L2
L3
surface
0.5
0.5
0.5
Notes: Here is a simple proof. We first project ½ for all lights, and capture the first image I0, which includes half the direct and half the global.
$I_0=\frac{1}{2}\sum_{i=1}^3 \left(L_d^{(i)}+L_g^{(i)}\right)$
$ I_i = \begin{cases}
I_0-L_d^{(i)}/2,\\
I_0+L_d^{(i)}/2,
\end{cases}
$

## Slide 23: A Theoretical Lower Bound for N Sources
L1
L2
L3
N+1 images are needed to extract the N direct components
surface
0/1
Binary
0.5
0.5
for points not directly lit by L1
for points directly lit by L1
Notes: Next, we change a pattern of L1 to black/white pattern and keep other lights unchanged.
Now, for points directly lit by L1, in this image, its intensities increase since they receive ½ more direct illumination from L1. For points not directly lit by L1, their intensities decreases since they receive ½ less direct illumination from L1. So we have this relationship.
$I_0=\frac{1}{2}\sum_{i=1}^3 \left(L_d^{(i)}+L_g^{(i)}\right)$
$ I_i = \begin{cases}
I_0-L_d^{(i)}/2,\\
I_0+L_d^{(i)}/2,
\end{cases}
$

## Slide 24: A Theoretical Lower Bound for N Sources
L1
L2
L3
N+1 images are needed to extract the N direct components
surface
0/1
Binary
0.5
for points not directly lit by L2
for points directly lit by L2
0.5
Notes: We have similar relations with I2 and I3.
$I_0=\frac{1}{2}\sum_{i=1}^3 \left(L_d^{(i)}+L_g^{(i)}\right)$
$ I_i = \begin{cases}
I_0-L_d^{(i)}/2,\\
I_0+L_d^{(i)}/2,
\end{cases}
$

## Slide 25: A Theoretical Lower Bound for N Sources
L1
L2
L3
N+1 images are needed to extract the N direct components
surface
0.5
0.5
0/1
Binary
for points not directly lit by L3
for points directly lit by L3
Notes: $I_0=\frac{1}{2}\sum_{i=1}^3 \left(L_d^{(i)}+L_g^{(i)}\right)$
$ I_i = \begin{cases}
I_0-L_d^{(i)}/2,\\
I_0+L_d^{(i)}/2,
\end{cases}
$

## Slide 26: A Theoretical Lower Bound for N Sources
L1
L2
L3
N+1 images are needed to extract the N direct components
surface
0.5
0.5
0/1
Binary
Notes: Now, given these N+1 images, we can estimate the direct illuminations using this equation.
$I_0=\frac{1}{2}\sum_{i=1}^3 \left(L_d^{(i)}+L_g^{(i)}\right)$
$ I_i = \begin{cases}
I_0-L_d^{(i)}/2,\\
I_0+L_d^{(i)}/2,
\end{cases}
$

## Slide 27: Practical Issues and The Solution
Difficult to create sharp step edges in illumination
  Cross-talk, color bleeding, screen door effect, defocus, etc.
Image intensity change is small, and sensitive to noise
  Only one source changes its pattern at a time
Solutions:
Use a shifting checkerboard pattern  lots of images
Use sinusoid patterns, one temporal frequency per light
Notes: In practice, however, it is difficult to create sharp step edges because of color bleeding and other problems. Moreover, for a large number light sources, changing only a single light will not change image intensity much and the difference will be noisy.
One could use a shifting checkerboard pattern to solve the problem of step edges, however it requires lots of images.
In this work, we proposed a method called frequency modulated multiplexing, which modulates each light with a unique temporal frequency sinusoid. It reduces the number of images needed, and it brings SNR benefits.

## Slide 28: Frequency Modulated Multiplexing
Modulate each source with a high-frequency sinusoid
Move modulation pattern with a unique speed per source
L1
L2
L3
surface
Key observation:
  For high-frequency illumination, the global illumination component stays unchanged when the modulation pattern shifts.
Notes: Here is the key idea.
We modulate each light source with a high spatial frequency sinusoid so that the global illumination stays constant.
We then move the modulation patterns, with a unique speed for each light source. Note that even when the patterns move, the global illumination does not change because the light patterns have high spatial frequencies.
But since the light patterns move at different speeds, each light source has a unique temporal frequency modulation. Therefore we can separate them.

## Slide 29: Frequency Modulated Multiplexing
L1
L2
L3
surface
Irradiance from sources at p at time t:
where
Notes: Here is the detailed derivation.
This is the total irradiance the point p receives from all the sources,
$L(t) = \sum_{i=1}^N
A_i\cdot\left(1+\sin\left(\omega_it+\phi_i\right)\right)/2$
$\omega_i=2\pi f u_i$

## Slide 30: Frequency Modulated Multiplexing
L1
L2
L3
surface
Radiance at p at time t:
Direct
Global
Notes: Suppose the point P’s reflectance is R, here is the reflected radiance at point p at at time t. The first term is the direct illumination and second term is global illumination.
We can expand this term and get this equation,
where
$L(t) = \sum_{i=1}^N
A_i\cdot\left(1+\sin\left(\omega_it+\phi_i\right)\right)/2$
$\omega_i=2\pi f u_i$
$I(t) = R\cdot L(t) + \frac{1}{2}\sum_{i=1}^N L_g^{(i)}$
\\
&=\sum_{i=1}^N\left(\alpha_i\sin\left(
\omega_it\right) +\beta_i\cos\left(\omega_it\right)\right) +
\frac{1}{\sqrt{2}}\gamma
\end{split}$

## Slide 31: Frequency Modulated Multiplexing
where
2N+1 images are sufficient to solve for direct components
Linear equation with respect to the 2N+1 unknowns
  cf. sequential separation with sinusoid has 3N unknowns
Notes: Alpha_i, beta_i, and gamma are defined as these.
Note that these are linear equations with respect to the unknowns alpha_i, beta_i, and gamma.
There are in total 2N+1 unknowns and thus 2N+1 images are sufficient to solve.
((Of course, alpha_i and beta_i are related.))
$\alpha_i=L_d^{(i)}\cos(\phi_i)/2$
$\beta_i=L_d^{(i)}\sin(\phi_i)/2$
$\gamma=\sum_{i=1}^N\left(L_d^{(i)}+L_g^{(i)}\right)/\sqrt{2}$
$L_d^{(i)}=2\sqrt{\alpha_i^2+\beta_i^2}$

## Slide 32: Frequency Modulated Multiplexing
Multiplexing Matrix F
Notes: We can write these 2N+1 linear equations in matrix form. Here is the multiplexing matrix F.
An interesting question to ask is what are the optimal frequencies and timings to use.

## Slide 33: Frequency Modulated Multiplexing
Multiplexing Matrix F
Optimal Condition: if the frequencies and timings satisfy
the matrix F becomes an orthogonal matrix with the minimum
condition number 1.
(Please refer to the paper for detailed proof.)
Notes: We prove that as long as the frequencies and timings satisfy this condition, the matrix F becomes an orthogonal matrix with the minimum condition number 1. Please refer to our paper for detailed proof.

## Slide 34: Experimental Results
Notes: Here I’d like to show you some experimental results.

## Slide 35
Projected
Patterns
Captured
Images
Light 1
Light 2
Light 3
Input: 3*2+1=7 images
Notes: Here is an example of a concave bowl.
Here are the input 7 images. The top shows the modulated light patterns. The bottom shows the captured images.

## Slide 36
Sequential Separation
[Nayar 2006]
Our Method
No Separation
Light 1
Light 2
Light 3
Direct Illumination
Notes: Here are the direct components.
In comparison, we show the results of sequential separation method which need 9 images.

## Slide 37: Estimated Normal and Depth Profile
Our Method (7 images)
Sequential Separation
[Nayar 2006] (9 images)
No Separation (3 images)
Depth Profiles
No Separation
Sequential
Ours
Notes: Here we show the recovered normal maps and depth profiles.
Our method uses fewer images and recovers better results.
We can notice an artifact on the sequential separation result, it shows a SNR benefit of multiplexed illumination.

## Slide 38: SNR Analysis
Similar conclusions as conventional light multiplexing
For dim light sources, SNR gain is
For bright scenes, no SNR benefit for multiplexing.
(Please refer to the paper for detailed derivation.)
Notes: We also analyzed SNR benefits of the proposed frequency modulated multiplexing. We obtain similar conclusions as conventional light multiplexing.
For dim light sources, we can have SNR gain of sqrt(2N+1)/sqrt(3).
For bright scenes where photon noise dominates, there is no SNR benefit of multiplexing.
Please refer to our paper for detailed derivations.
$\mbox{Trace}\left((\mathbf{F}^T\mathbf{F})^{-1}\right)-(\mathbf{F}^T\mathbf{F})^{-1}_{2N+1,2N+1}=\frac{4N}{2N+1}$

## Slide 39: 1. V-Groove (Photometric Stereo, N=3)
Our Method
(7 images)
No Separation
(3 images)
Extracted 3 Direct Illumination
Notes: Here is an example of using photometric stereo for a V-groove

## Slide 40: 1. V-Groove (Photometric Stereo, N=3)
Normal
Albedo
Our Method
No Separation
Depth Profile
Ground
Truth
Ours
No Separation
Notes: Here are the recovered results. As shown, with separation we can obtain more accurate surface normals and depths.

## Slide 41: 2. Christmas Scene (Phase Shifting: N=3)
Candle
Flower
Fabric
V-groove
Notes: Here is an example of phase shifting to recover scene depth. We construct the scene to include both inter-reflection and subsurface scattering.

## Slide 42
Projected
Patterns
Captured
Images
Light 1
Light 2
Light 3
Input: 3*2+1=7 images
Notes: Here are the input images.

## Slide 43: Depth Error (w.r.t Ground Truth)
No Separation
(3 images)
Sequential (Checkerboard)
[Nayar 2006] (75 images)
Our Method
(7 images)
Sequential (Sinusoid)
[Nayar 2006] (9 images)
Notes: Here are the errors of the recovered depths with respect to ground truth.
As shown, our method obtains the best result, using much fewer images than the sequential separation method.

## Slide 44: 3. Cake Mold (Normal & BRDF, N=9)
Notes: In the last example, we use 9 light sources to recover the normals and BRDF of a cake mold.

## Slide 45: Direct Illuminations of N=9 Lights
No Separation
(9 images)
Our Method
(2*9+1=19 images)
Notes: Here are the extract direct illuminations.

## Slide 46: Estimated Normal and Depth
No Separation
(9 images)
Our Method
(2*9+1=19 images)
Notes: Here we show the recovered normals, and the depth, with respect to the ground truth.

## Slide 47: Estimated Normal and Depth
No Separation
(9 images)
Our Method
(2*9+1=19 images)
Ground
Truth Depth
Notes: Here we show the recovered normals, and the depth, with respect to the ground truth.

## Slide 48: Estimated BRDF
No Separation
(9 images)
Ground Truth
Our Method
(2*9+1=19 images)
Notes: Here we show the renderings of the recovered BRDFs. Our method obtains much more accurate results.

## Slide 49: Summary
We proposed a method to extract direct illuminations for multiple light sources with fewer images.
For dim light sources, the proposed method has SNR advantage because of illumination multiplexing.
http://www.cis.rit.edu/jwgu/research/demux
More experimental results are:
Notes: More experimental results can be found at our project webpage.
In summary we proposed a method to extract direct illuminations from multiple light sources with fewer images.
We showed that for dim light sources, the proposed method has SNR advantage because of illumination multiplexing.
Pause for 5 seconds.

## Slide 50: Global Illumination Can Be Useful.
Notes: So far, we have considered global illumination as noise – something which needs to be removed.
But if we think about it, global illumination can be useful. It encodes intra-scene optical interactions. If we can recover global illumination, we can learn a lot of things about the scene.

## Slide 51: Future Work: Using Global Illumination for Scene Recovery
Direct Component
Global Component
Scene
Notes: Here is an example. This is a scene with a variety of organic materials, fruits and vegetables. The global component image is really beautiful to look at…
From a computer vision point of view, this separation is useful as well. It can be used to make material and geometric inferences about the scene. For the fruits, we can notice that the global component is much higher as compared to the direct component. This is because of sub-surface scattering. It indicates presence of translucent materials. We can notice high global component between the eggs. This is because of inter-reflections. It indicates presence of local concave structures.

## Slide 52
Light Source
Scene
Inter-reflections
Sub-surface scattering
Volumetric Scattering
Direct Illumination
Future Work: Decomposing Global Illumination
Notes: Now, we know how to separate the direct and global components. In the future, we want to decompose global illumination further into its various components – interreflections, subsurface scattering and volumetric scattering, as each component tells us something different about the scene.
The message that I would like to leave you with is that there is a lot of information hidden in these light transport effects. We are trying to figure out how to extract it. Once we do, we will have taken significant steps towards building vision systems which can understand the scene.
Thank you very much, and I will be happy to take any questions.

## Slide 53
Light Source
Scene
Inter-reflections
Sub-surface scattering
Volumetric Scattering
Direct Illumination
Future Work: Decomposing Global Illumination
Notes: Now, we know how to separate the direct and global components.

## Slide 54
Light Source
Scene
Inter-reflections
Sub-surface scattering
Volumetric Scattering
Direct Illumination
Future Work: Decomposing Global Illumination
Notes: In the future, we want to decompose global illumination further into its various components – interreflections, subsurface scattering and volumetric scattering, as each component tells us something different about the scene.
The message that I would like to leave you with is that there is a lot of information hidden in these light transport effects. We are trying to figure out how to extract it. Once we do, we will have taken significant steps towards building vision systems which can understand the scene.
Thank you very much, and I will be happy to take any questions.

## Slide 56: Summary
A theoretical lower bound
  N+1 images are needed for extracting the N direct illuminations for N light sources.
An optimal Frequency Modulated Multiplexing scheme
  2N+1 images are sufficient for extracting the N direct illuminations for N light sources
SNR analysis of illumination multiplexing in the presence of global illumination
  sqrt(N) SNR gain if read noise dominates
  2/3 SNR gain if photon noise dominates
Notes: Xxx
Multiple light sources
If we only care about the direct illumination, can we do better?
Two key insights:
  Global illumination stays unchanged, as long as high frequency patterns are …
  Multiplexed illumination can have SNR benefits …

## Slide 57: Limitations & Future Work
Only direct illumination components are extracted.
The use of the recovered phase maps.
What is the minimal number of images required, for different types of scenes?

## Slide 58: Conventional Hadamard Multiplexing for Direct/Global Separation

## Slide 59: Experimental Comparison
Frequency modulated multiplexing needs fewer images while provide a better estimate for direct illumination.

## Slide 60: Simulation Results
Ground truth global illumination is estimated by radiosity

## Slide 61: SNR Analysis: Simulation Results
N=30 lights

## Slide 62: Input Images
Our Method
(3*2+1=7 images)
Sequential Separation
with Checkerboard [Nayar 2006]
(3*25=75 images)
Sequential Separation
with Sinusoid
[Nayar 2006]
(3*3=9 images)

## Slide 63: Evaluation (Read Noise)
SSIM
SSIM
0.86
0.77
0.57
0.21
0.88
0.86
0.77
0.46
Noise
0.005
0.01
0.02
0.05
Sinusoid
Sequential
(3N images)
Frequency
Modulated
Multiplexing
(2N+1 images)

## Slide 64: Evaluation (Photon Noise)
SSIM
SSIM
0.88
0.85
0.74
0.43
0.88
0.83
0.71
0.36
Noise
0.005
0.01
0.02
0.05
Sinusoid
Sequential
(3N images)
Frequency
Modulated
Multiplexing
(2N+1 images)

## Slide 65: SNR Analysis
Similar conclusions as conventional light multiplexing
Require fewer input images (2N+1), and thus faster
Dim
Scenes
Bright
Scenes
Conventional
Multiplexing
(3N images)
No Multiplexing
(3N images)
Compared to
Read
Noise:
Photon
Noise:
SNR Gain
SNR reduces by
(Please refer to the paper for detailed derivation.)
Notes: $\mbox{Trace}\left((\mathbf{F}^T\mathbf{F})^{-1}\right)-(\mathbf{F}^T\mathbf{F})^{-1}_{2N+1,2N+1}=\frac{4N}{2N+1}$

## Slide 66
p=0
p=2/3π
p=4/3π
Sequential Separation
[Nayar 2006]
Our Method
No Separation
Light 1
Light 2
Light 3
Direct Illumination

## Slide 67: (Sum of) Global Illumination
Sequential Separation
[Nayar 2006]
Our Method

## Slide 68: 4. Pop-up Book (Phase Shifting, N=3)

## Slide 69
Projected
Patterns
Captured
Images
Light 1
Light 2
Light 3
Input: 3*2+1=7 images

## Slide 70: Depth Maps
Ground Truth
No Separation
Checkerboard
[Nayar 2006]
Our Method

## Slide 71: Depth Errors (w.r.t. Ground Truth)
No Separation
(3 images)
Sequential Separation
with Checkerboard [Nayar 2006]
(3*25=75 images)
Our Method
(2*3+1=7 images)